## Slide 1: Coxswain Authority & Responsibility

## Slide 2: Coxswain Authority & Responsibility
In Order of Precedence
Safety & Conduct of passengers of crew.
Safe Operation & Navigation of the boat assigned.
Completion of the sortie or mission.
Ref. CIM 5000.3 (series)CH.5 Part 1 (5-1-8)

## Slide 3: Coast Guard Auxiliary Purpose
In accordance with (IAW) 14 USC 822 to assist Coast Guard:
Promote safety and effect rescues.
Promote efficient operation of motorboats & yachts.
Foster knowledge of compliance w/laws, rules & regulations.
Facilitate other operations for Coast Guard.
Ref. CIM 5000.3 (series) CH1 Part 4 (1-4-2)

## Slide 4: Fire Fighting Policy Task COXN 03-03-Aux
Independent firefighting. CG personnel shall not engage in independent fire fighting operations, except to save a life or in the early stages of a fire to avert a significant threat without undue risk.
Commercial vessels & waterfront facilities. CG personnel shall not actively engage in fire fighting except in support of a regular firefighting agency under the supervision of a qualified fire officer.
Ref. (IAMSAR) CIM 16130.2(series)(4.4.2.2)

## Slide 5: General Salvage Other than Towing Task COXN 03-03-Aux
CG Units may assist within capabilities, if salvor requests. When no commercial salvage facilities are on scene, CG units should only engage (e.g. ungrounding, pumping, damage control) to prevent a worsening situation.
Any salvage operations shall be performed at the discretion of the unit CO/OINC.
CG units & personnel shall not be unduly hazarded in performing salvage.
Ref (IAMSAR) CIM 16130.2 (series) (4.3.1)

## Slide 6: Operator Insistence Task COXN 09-03-Aux
Occasionally an operator will insist that the CG act, such as ungrounding their vessel. CG is under no obligation.
If a decision to comply with such request it should be made clear that the operator is assuming the risk of the operation.
The fact that the action is undertaken at operator’s request, and is against CG advice, should be logged.
Ref. (IAMSAR) CIM 16130.2 (series) (4.3.3)

## Slide 7: Maximum Underway (Fatigue) Hours) Underway Limits Task COXN 02-01-Aux
Boat Size | Seas <4 FT | Seas > 4 FT | Rest Hours Required
30 FT & above | 8 hours | 8 hours | 8 hours
Less Than 30 FT | 8 hours | 0 | 8 hours
PWC no seas greater than 3 FT | 6 hours | N/A | 1 hour required after 3 hrs
Trailering | 350 miles (total) or 8 hours |  | 
Ref. AOPG Vol 1 CH10 (Sec L.6.) Table 10-3

## Slide 8: (Fatigue) Hours Trailering
Trailering hours shall be counted towards crew fatigue limitations for boat crews. (For fatigue standards, 1 hour of trailering counts as 30 minutes towards crew fatigue computation).
Trailering for any Auxiliary activity under orders shall not exceed 350 miles (total) or 8 hours in a 24-hour period.
Ref. AOPG Vol 1 CH10 (Sec L.6.)

## Slide 9: Fatigue Personnel
Fatigued personnel may not realize when their physical or metal state is compromised.
Decreased coordination
Narrow attention span
Lower standard of performance
Judgement errors in boat handling, seamanship, mission decisions
Show decreased concern for safety
Cut corners
Ref: AOPG CH 10 (Sec L.1.)

## Slide 10: Fatigue Waiver
Authority for fatigue waivers resides with the Operational Commander (OPCON), only after the OIA requests a waiver.
Ref: AOPG Vol 1 CH10 (Sec F.5.)

## Slide 11: Requesting Waiver Information
Facility identification(e.g. hull number, Patrol Order number)
Type of waiver (e.g. disabling casualty, fatigue, crewing)
Specific condition to be waived (e.g. inop bilge pump, Nighttime certification)
Conditions and risk management measures (e.g. stay within sight of other CG asset, additional coxswain, PPE on board)
Waivers requiring Operational Commander, DIRAUX or OIA approval shall include:
Ref: AOPG Vol 1 CH10 (Sec F.7.) // BSX PL 24-01

## Slide 12: Waiver Documentation
Waiver approvals may be a letter, memo, e-mail or AUXDATA II entry and shall include:
Date & time waiver was granted,
Name & rank of who granted waiver,
Detail capturing what operations are restricted & mitigating actions to reduce risk.
A verbal waiver is authorized but shall be followed with a (written waiver within 4 hours).
Ref: AOPG Vol 1 CH.10 (Sec F.8.)

## Slide 13: Minimum Crew Requirement Task COXN 02-01-Aux
Vessel Length (Feet) | Coxswain | Crew
< 26 | 1 | 1
> 26 < 40 | 1 | 2
> 40 < 65 | 1 | 3
> 65 | 1 | 4
PWC | 1 | 0
Coxswains cannot substitute trainees or uncertified members for any of the crew requirements on surface facilities.
AOPG Vol 1 CH 10 (Sec. E.2.)

## Slide 14: Minimum Boat Crew Requirement Waiver
Waivers for the minimum boat crew requirements may be granted by the DIRAUX in cases where the OTO is satisfied that a smaller crew can safely operate the facility.
Ref: AOPG Vol 1 CH.10 (Sec F.3.)

## Slide 15: Safe Haven Considerations
In cases involving towing the vessel being assisted will normally be taken to the nearest safe haven that has available means of communication. CG or Auxiliary resources should not tow the vessels beyond the nearest safe haven.
Exceptions to this policy may be made if specific cases if, in the judgment of the SMC, they are warranted by humanitarian or other concerns.
Reluctance of private firms, Yacht clubs & attendant potential liability.
(IAMSAR) CIM 16130.2 (series) (4.1.6.5.)

## Slide 16: Disabling Casualties
Disabling casualties are those that make the boat Not Mission Capable (NMC)
Ref: AOPG Vol 1 CH.10 (Sec C.3.)

## Slide 17: List of Disabling Casualties Task COXN 03-03-Aux
Engine and Vessel Systems
Engine(s) metallic/non-metallic noises: abnormal metal on metal/knock/clicking.
Engine(s) fail to start
Engine(s) overheat (uncontrollable).
Engine kill switch (motor safety lanyard)inoperable or missing.
Engine controls(throttle & shift) inoperable.
Engine(s) fail to shift into & out of gear (forward or reverse)
Battery system won’t charge.
Steering system inoperable or restricted(binding or less than full movement).
Any fuel leaks on gasoline engines.
Ref: AOPG Vol 1 CH.10 (Sec C.4.)

## Slide 18: List of Disabling Casualties Task COXN 03-03-Aux
Electronics / Navigation
No electronic means of signaling distress (i.e. no radio or PLB)
Boat Outfit
Bilge pump fails to operate or clearing ports clogged or restricted (if installed).
Safety & General Material
Any electrical arcing & sparking.
Any hull breach below the waterline or structural damage that weakens the transom.
No means of firefighting (i.e. no portable fire extinguishers plus installed fire system inoperable)
Backfire flame arrester inoperable or missing, if required.
Ref: AOPG Vol 1 CH.10 (Sec C.4.)

## Slide 19: Disabling Actions (Underway)
In the event a facility sustains a disabling casualty while underway, the OIA shall immediately be notified determine whether to continue the mission or return to home port or safe mooring.
The OIA shall notify OPCON as soon as possible once the disabling casualty is identified and what actions are taken to mitigate any further damage.
OPCON will have final authority to authorize the facility to transit back to home port or safe mooring after an evaluation of the potential risk.
Ref: AOPG Vol 1 CH.10 (Sec C.3.a.)

## Slide 20: Disabling Actions (Dockside)
If a disabling casualty is identified while the facility is moored, the facility is not authorized to get underway for a mission until the discrepancy is fully repaired.
Ref: AOPG Vol 1 CH.10 (Sec C.3.b.)

## Slide 21: Restrictive Discrepancies Task COXN 03-03-Aux
Restrictive discrepancies restrict the operation of the facility such that it can perform some, but not all, activities safely.
Facilities w/ restrictive discrepancies shall be in a NMC status.
DIRAUX, after conducting risk management, may issue a written waiver (IAW) Chapter 10 Section F.
If a waiver is issued, the facility will be upgraded to Partially Mission Capable (PMC)
Ref:AOPG Vol 1. CH.10 (Sec C.5.)

## Slide 22: List of Restrictive Discrepancies Task COXN 02-01-Aux
Engine and Vessel Systems
Engine(s) alarms inoperative (i.e. high-water temperature)(if installed)
Engine alarms inoperative (i.e. low oil pressure-if installed)
Electronics / Navigation
Radio inoperable.
Radar inoperable, if so equipped (for night operation or less than one mile visibility).
Fathometer inoperable. (if installed)
GPS/DGPS inoperable. (if installed)
Navigation light(s) inoperative.
Ref: AOPG Vol 1 CH.10 (Sec C.6.)

## Slide 23: Restrictive Actions (Underway)
In the event a facility sustains a restrictive discrepancy while U/W, the coxswain shall immediately notify the OIA w/all pertinent information.
After boat crew evaluates potential risks, the coxswain provides a recommendation of whether to continue that mission.
Ref: AOPG Vol 1 CH.10 (Sec C.5.a.)

## Slide 24: Restrictive Actions (Dockside) Task COXN 03-03-Aux
Facilities shall not get underway until the discrepancy is repaired, or a waiver has been granted (IAW) Chapter 10 Section F.

## Slide 25: PPE Requirements Task COXN 03-03-Aux

## Slide 26: PPE Waiver
The Operational Commander (OPCON) or CO/OIC may waive, on a single sortie basis, the wearing of hypothermia protective device, if the degree of risk of hypothermia is minimal (e.g. non-hazardous, daylight operations in calm water).
The operator may request a waiver thru the OIA, when there is concern about adverse effect of “thermal stress”.
Auxiliarist are still required to carry waived hypothermia protective device onboard the facility.
Ref: AOPG Vol 1 CH.10 (Sec F.6.)

## Slide 27: Night Certification Waiver
The requirement for a fully nighttime certified boat crew may be waived, on a case-by-case basis in order to complete the mission.
Clear communication & complete understanding between the OIA & the coxswain. In instances where the waiver has been granted by the OIA, the final decision regarding the safety of continuing the mission rests with the coxswain unless otherwise assessed by the OIA based on available information.
Ref: BSX Policy Letter 24-01

## Slide 28: Night Operations Waiver (Underway)
If underway, the coxswain identifies that the facility doesn’t have a complete crew that is certified to conduct night operations must seek a waiver to operate past sunset from the OIA as soon as it becomes apparent to any of the crew there is a possibility for the facility to remain u/w past sunset.
This includes when a tow will extend past sunset, response to SAR case will require operations past sunset, or a return transit to mooring.
OIA verbal granting of waiver is authorized.
Comments shall be added by the OIA to the Patrol Order that waiver was issued.
Ref: BSX Policy Letter 24-01

## Slide 29: Night Operations Waiver (Moored)
If not u/w with the possibility that the facility’s operations will extend beyond sunset, for any reason, then the coxswain must obtain a waiver, following the requirements IAW AOPG Vol 1, CH.10 (Sec F.7.) prior to requesting patrol order or getting underway w/ approved patrol orders.
Authority for granting waiver resides with the OIA.
Ref. BSX Policy Letter 24-01

## Slide 30: Conclusion
Types of Waivers
Fatigue
Minimum Crew Requirements
Restrictive
PPE
Night Certification
Ref: AOPG Vol 1 CH.10 (Sec F.1.)

## Slide 31: Waiver Authority Simplified
Waiver Type | Thru | Granting Authority
Fatigue | OIA/ SECTOR | Operational Commander
Minimum Crew Requirement | OIA / SECTOR | DIRAUX /OTO
Restrictive | OIA / SECTOR | DIRAUX / OTO
PPE | OIA / SECTOR | Operational Commander/ CO/OIC
Night Certification | OIA / SECTOR | OIA

## Slide 32: C. Y. A.
Can You Articulate
Identify the discrepancy
Notify the proper chain of command
Request waiver through the proper authority

## Slide 33: In Service to our Nation With Honor, Respect, and Devotion to Duty We protect We defend We save We are Semper Paratus We are the United States Coast Guard